INIT
Linux Start up & Shutdown Process
Thanks to:
Jalal Hajiqholamali
Amir Hossein Eshaghi

---
What is INIT?
init (short for initialization) is the program on Unix and Unix-like systems that spawns all other processes. It runs as a daemon and typically has PID 1.
The functionality diverged, in Unixes such as System III and System V, from the functionality provided by the init in Research Unix and its BSD derivatives.
The usage on most Linux distributions is compatible with System V, but some distributions, such as Arch and Slackware, use a BSD-style and others, such as Gentoo, have their own customized version.
Ubuntu and some other Linux distros now use upstart as a replacement for the traditional Init process.

---
What happens when you turn a Linux computer on?
The BIOS performs hardware-platform specific startup tasks.
The BIOS or firmware system reads the master boot record (MBR) on the harddisk or other boot device (for example, CD, floppy, netboot, etc.).
A boot loader runs. Linux systems on x86 systems typically use LILO or GRUB. In general, a boot loader is a simple program that knows where to look for the Linux kernel, perhaps choosing among several versions or even selecting other operating systems on the same machine.
[The BIOS loads and executes the partition boot code from the designated boot device, which contains phase 1 of a Linux boot loader. Phase 1 loads phase 2 (the bulk of the boot loader code). Some loaders may use an intermediate phase (known as phase 1.5) to achieve this since modern large disks may not be fully readable without further code.]

---
What happens when you turn a Linux computer on?
The kernel loads.
The root filesystem is mounted. In some cases, a temporary ramdisk image is loaded before the true root filesystem to enable special drivers or modules that might be necessary for the true root filesystem.
The first thing the kernel does is to execute init program. Init is the root/parent of all processes executing on Linux.
The first processes that init starts is a script /etc/rc.d/rc.sysinit

---
Init Call Mechanism in the Linux Kernel
Notice: start_kernel() supporting functions are changed from version to version, as they depend on OS component internals, which are being improved all the time. (These are for Kernel 2.6.34 and X86 Machine and for 32bit)
Step 1. in linux/arch/x86/kernel/head32.c call start_kernel()
You can see this file source in: http://lxr.linux.no/#linux+v2.6.34/arch/x86/kernel/head32.c
/*
   2 * linux/arch/i386/kernel/head32.c -- prepare to run common code
   3 *
   4 * Copyright (C) 2000 Andrea Arcangeli <andrea@suse.de> SuSE
   5 * Copyright (C) 2007 Eric Biederman <ebiederm@xmission.com>
   6 */
   7
   8#include <linux/init.h>
   9#include <linux/start_kernel.h>
  10#include <linux/mm.h>
  ....

---
Init Call Mechanism in the Linux Kernel
31void __init i386_start_kernel(void)
  32{
  33#ifdef CONFIG_X86_TRAMPOLINE
...
  39 reserve_early_overlap_ok(PAGE_SIZE, PAGE_SIZE + PAGE_SIZE,
  40 "EX TRAMPOLINE");
  41#endif
  42
  43 reserve_early(__pa_symbol(&_text), __pa_symbol(&__bss_stop), "TEXT DATA BSS");
  44
  45#ifdef CONFIG_BLK_DEV_INITRD
  46 /* Reserve INITRD */
  47 if (boot_params.hdr.type_of_loader && boot_params.hdr.ramdisk_image) {
  48 /* Assume only end is not page aligned */
  49 u64 ramdisk_image = boot_params.hdr.ramdisk_image;
  50 u64 ramdisk_size = boot_params.hdr.ramdisk_size;
  51 u64 ramdisk_end = PAGE_ALIGN(ramdisk_image + ramdisk_size);
  52 reserve_early(ramdisk_image, ramdisk_end, "RAMDISK");
  53 }
  54#endif
...
  72 start_kernel();
  73}

---
Init Call Mechanism in the Linux Kernel
And define the prototype for start_kernel in header file linux/include/linux/start_kernel.h
You can see this file source in: http://lxr.linux.no/#linux+v2.6.34/include/linux/start_kernel.h
   1#ifndef _LINUX_START_KERNEL_H
   2#define _LINUX_START_KERNEL_H
   3
   4#include <linux/linkage.h>
   5#include <linux/init.h>
   6
   7/* Define the prototype for start_kernel here, rather than cluttering
   8 up something else. */
   9
  10extern asmlinkage void __init start_kernel(void);
  11
  12#endif /* _LINUX_START_KERNEL_H */

---
Init Call Mechanism in the Linux Kernel
Step 2. in linux/init/main.c , start_kernel() calls rest_init() to spawn an "init" process and become "idle" process itself.
You can see this file source in: http://lxr.linux.no/#linux+v2.6.34/init/main.c
 528asmlinkage void __init start_kernel(void)
 529{
...
 553/*
 554 * Interrupts are still disabled. Do necessary setups, then
 555 * enable them
 556 */
 557 lock_kernel();
 558 tick_init();
 559 boot_cpu_init();
 560 page_address_init();
 561 printk(KERN_NOTICE "%s", linux_banner);
 562 setup_arch(&command_line);
 563 mm_init_owner(&init_mm, &init_task);
 564 setup_command_line(command_line);
 ...
 696
 697 /* Do the rest non-__init'ed, we're now alive */
 698 rest_init();
 699}

---
Init Call Mechanism in the Linux Kernel
Step 3. in linux/init/main.c , "Init" process
You can see this file source in: http://lxr.linux.no/#linux+v2.6.34/init/main.c
static int __init kernel_init(void * unused)
 855{
 856 lock_kernel();
 857
 858 /*
 859 * init can allocate pages on any node
 860 */
 861 set_mems_allowed(node_states[N_HIGH_MEMORY]);
 862 /*
 863 * init can run on any cpu.
 864 */
 865 set_cpus_allowed_ptr(current, cpu_all_mask);
 866 /*
 867 * Tell the world that we're going to be the grim
 868 * reaper of innocent orphaned children.
 869 *
 870 * We don't want people to have to make incorrect
 871 * assumptions about where in the task array this
 872 * can be found.
 873 */
 874 init_pid_ns.child_reaper = current;
 875
 876 cad_pid = task_pid(current);

---
Init Call Mechanism in the Linux Kernel
 878 smp_prepare_cpus(setup_max_cpus);
 880 do_pre_smp_initcalls();
 881 start_boot_trace();
 883 smp_init();
 884 sched_init_smp();
 886 do_basic_setup();
 888 /* Open the /dev/console on the rootfs, this should never fail */
 889 if (sys_open((const char __user *) "/dev/console", O_RDWR, 0) < 0)
 890 printk(KERN_WARNING "Warning: unable to open an initial console.\n");
 892 (void) sys_dup(0);
 893 (void) sys_dup(0);
 895 /** check if there is an early userspace init. If yes, let it do all
 896 * the work */
 899 if (!ramdisk_execute_command)
 900 ramdisk_execute_command = "/init";
 902 if (sys_access((const char __user *) ramdisk_execute_command, 0) != 0) {
 903 ramdisk_execute_command = NULL;
 904 prepare_namespace();
 905 }
 907 /* * Ok, we have completed the initial bootup, and
 909 * we're essentially up and running. Get rid of the
 910 * initmem segments and start the user-mode stuff.. */
 913 init_post();
 914 return 0;
 915}

---
The Linux Init Processes
The init process is the last step in the boot procedure and identified by process id "1".
Its primary role is to create processes from a script stored in the file /etc/inittab .
This file usually has entries which cause init to spawn gettys on each line that users can log in.
It is a user process and not a kernel system process although it does run as root.
Upon shutdown, init controls the sequence and processes for shutdown. The init process is never shut down.

---
/etc/inittab
The inittab file describes which processes are started at bootup and during normal operation. An entry in the inittab file has the following format (Lines beginning with '#' are ignored.):
    id:runlevels:action:process
id
is a unique sequence of 1-4 characters which identifies an entry in inittab.
runlevels
lists the runlevels for which the specified action should be taken.
action
describes which action should be taken.
process
specifies the process to be executed.

---
/etc/inittab
# inittab This file describes how the INIT process should set up
# the system in a certain run-level.
# Author: Miquel van Smoorenburg, <miquels@drinkel.nl.mugnet.org>
# Modified for RHS Linux by Marc Ewing and Donnie Barnes
# Default runlevel. The runlevels used by RHS are:
# 0 - halt (Do NOT set initdefault to this)
# 1 - Single user mode
# 2 - Multiuser, without NFS (The same as 3, if you do not have networking)
# 3 - Full multiuser mode
# 4 - unused
# 5 - X11
# 6 - reboot (Do NOT set initdefault to this)
#
id:5:initdefault:
# System initialization.
si::sysinit:/etc/rc.d/rc.sysinit
l0:0:wait:/etc/rc.d/rc 0
l1:1:wait:/etc/rc.d/rc 1
l2:2:wait:/etc/rc.d/rc 2
l3:3:wait:/etc/rc.d/rc 3
l4:4:wait:/etc/rc.d/rc 4
l5:5:wait:/etc/rc.d/rc 5
l6:6:wait:/etc/rc.d/rc 6

---
/etc/inittab
# Trap CTRL-ALT-DELETE
ca::ctrlaltdel:/sbin/shutdown -t3 -r now
# When our UPS tells us power has failed, assume we have a few minutes
# of power left. Schedule a shutdown for 2 minutes from now.
# This does, of course, assume you have powerd installed and your
# UPS connected and working correctly.
pf::powerfail:/sbin/shutdown -f -h +2 "Power Failure; System Shutting Down"
# If power was restored before the shutdown kicked in, cancel it.
pr:12345:powerokwait:/sbin/shutdown -c "Power Restored; Shutdown Cancelled"
# Run gettys in standard runlevels
1:2345:respawn:/sbin/mingetty tty1
2:2345:respawn:/sbin/mingetty tty2
3:2345:respawn:/sbin/mingetty tty3
4:2345:respawn:/sbin/mingetty tty4
5:2345:respawn:/sbin/mingetty tty5
6:2345:respawn:/sbin/mingetty tty6
# Run xdm in runlevel 5
x:5:respawn:/etc/X11/prefdm -nodaemon

---
/etc/inittab - Actions
Valid actions for the action field are:
respawn: The process will be restarted whenever it terminates (e.g. getty).
wait: The process will be started once when the specified runlevel is entered and init will wait for its termination.
once: The process will be executed once when the specified runlevel is entered.
boot: The process will be executed during system boot. The runlevels field is ignored.
bootwait: The process will be executed during system boot, while init waits for its termination (e.g. /etc/rc). The runlevels field is ignored.
off: This does nothing.

---
/etc/inittab - Actions
ondemand: A process marked with an ondemand runlevel will be executed whenever the specified ondemand runlevel is called. However, no runlevel change will occur (ondemand runlevels are 'a', 'b', and 'c').
initdefault: An initdefault entry specifies the runlevel which should be entered after system boot. If none exists, init will ask for a runlevel on the console. The process field is ignored.
sysinit: The process will be executed during system boot. It will be executed before any boot or bootwait entries. The runlevels field is ignored.
powerwait: The process will be executed when the power goes down. Init is usually informed about this by a process talking to a UPS connected to the computer. Init will wait for the process to finish before continuing.

---
/etc/inittab - Actions
powerfail: As for powerwait, except that init does not wait for the process's completion.
powerokwait: This process will be executed as soon as init is informormed that the power has been restored.
powerfailnow: This process will be executed when init is told that the battery of the external UPS is almost empty and the power is failing.
ctrlaltdel: The process will be executed when init receives the SIGINT signal. This means that someone on the system console has pressed the CTRL-ALT-DEL key combination.
kbrequest: The process will be executed when init receives a signal from the keyboard handler that a special key combination was pressed on the console keyboard.

---
RUNLEVELS
A runlevel is a software configuration of the system which allows only a selected group of processes to exist. The processes spawned by init for each of these runlevels are defined in the /etc/inittab file.
Init can be in one of eight runlevels: 0-6 and S or s.
Runlevels 0, 1, and 6 are reserved. Runlevel 0 is used to halt the system, runlevel 6 is used to reboot the system, and runlevel 1 is used to get the system down into single user mode.
Runlevel "3" will boot to text or console mode and "5" will boot to the graphical login mode ( "4" for slackware).

---
RUNLEVELS
Runlevel	Scripts Directory / (Red Hat/Fedora Core)	State
0	/etc/rc.d/rc0.d/	shutdown/halt system
1	/etc/rc.d/rc1.d/	Single user mode
2	/etc/rc.d/rc2.d/	Multiuser with no network services exported
3	/etc/rc.d/rc3.d/	Default text/console only start. Full multiuser
4	/etc/rc.d/rc4.d/	Reserved for local use. Also X-windows (Slackware/BSD)
5	/etc/rc.d/rc5.d/	XDM X-windows GUI mode (Redhat/System V)
6	/etc/rc.d/rc6.d/	Reboot
s or S		Single user/Maintenance mode (Slackware)
M		Multiuser mode (Slackware)

---
/etc/inittab – Some Examples
The first processes that init starts is a script /etc/rc.d/rc.sysinit
Runlevel-neutral system initialization. Generally there are some initialization actions that are performed regardless of runlevel. These steps are indicated in /etc/inittab with a line like:
# System initialization.
si::sysinit:/etc/rc.d/rc.sysinit
On some Linux systems (mostly Debian-based systems), you will see something more like:
si::sysinit:/etc/init.d/rcS
If the latter case, /etc/init.d/rcS is a script that simply runs each of the scripts matching /etc/rcS.d/[Ss]??*. On the other hand, if your system uses /etc/rc.d/rc.sysinit, that file contains a single long script to perform all the initialization.

---
/etc/rc.sysinit
#!/bin/bash
#
# /etc/rc.d/rc.sysinit - run once at boot time
#
# Taken in part from Miquel van Smoorenburg's bcheckrc.
#
HOSTNAME=$(/bin/hostname)
set -m
if [ -f /etc/sysconfig/network ]; then
    . /etc/sysconfig/network
fi
if [ -z "$HOSTNAME" -o "$HOSTNAME" = "(none)" ]; then
    HOSTNAME=localhost
fi
if [ ! -e /proc/mounts ]; then
mount -n -t proc /proc /proc
mount -n -t sysfs /sys /sys >/dev/null 2>&1
fi

---
/etc/inittab – Some Examples
You may actually define as many actions as you like related to runlevel, and each action may pertain to one or more runlevels. As a rule, /etc/inittab will contain some lines like:
l0:0:wait:/etc/rc.d/rc 0
# ...
l5:5:wait:/etc/rc.d/rc 5
l6:6:wait:/etc/rc.d/rc 6
In turn, the script /etc/rc.d/rc will run all the files matched by the pattern /etc/rc$1.d/[KkSs]??*. For example, on the sample system described that starts at runlevel 5, we would run (in order):
/etc/rc5.d/K15postgresql
/etc/rc5.d/S01switchprofile
/etc/rc5.d/S05harddrake
...
/etc/rc5.d/S55sshd
...
/etc/rc5.d/S99linuxconf
/etc/rc5.d/S99local

---
/etc/inittab – Some Examples
The files(s) starting with "K" or "k" are kill scripts that end processes or clean up their actions.
Those starting with "S" or "s" are startup scripts that generally launch new processes or otherwise prepare the system to run at that runlevel.
Most of these files will be shell scripts, and most will be links (often to files in /etc/init.d/).

---
Some files in /etc/rc5.d
lrwxrwxrwx. 1 root root 16 Jun 4 20:43 K01smartd -> ../init.d/smartd
lrwxrwxrwx. 1 root root 15 Jun 4 20:45 K01smolt -> ../init.d/smolt
lrwxrwxrwx. 1 root root 14 Jun 4 20:43 K05innd -> ../init.d/innd
lrwxrwxrwx. 1 root root 19 Jun 4 20:41 K10dc_server -> ../init.d/dc_server
lrwxrwxrwx. 1 root root 16 Jun 4 20:27 K10psacct -> ../init.d/psacct
lrwxrwxrwx. 1 root root 19 Jun 4 20:38 K10saslauthd -> ../init.d/saslauthd
lrwxrwxrwx. 1 root root 15 Jun 5 04:16 K10zvbid -> ../init.d/zvbid
lrwxrwxrwx. 1 root root 19 Jun 4 20:41 K12dc_client -> ../init.d/dc_client
lrwxrwxrwx. 1 root root 15 Jun 4 20:37 K15httpd -> ../init.d/httpd
lrwxrwxrwx. 1 root root 15 Jun 4 21:02 K20jetty -> ../init.d/jetty
lrwxrwxrwx. 1 root root 14 Jun 4 20:27 K24irda -> ../init.d/irda
lrwxrwxrwx. 1 root root 15 Jun 4 20:43 K25squid -> ../init.d/squid
lrwxrwxrwx. 1 root root 22 Jun 4 20:59 K30spamassassin -> ../init.d/spamassassin
lrwxrwxrwx. 1 root root 18 Jun 4 20:46 K35backuppc -> ../init.d/backuppc
lrwxrwxrwx. 1 root root 17 Jun 4 20:43 K35dovecot -> ../init.d/dovecot
lrwxrwxrwx. 1 root root 13 Jun 4 20:39 K35nmb -> ../init.d/nmb
lrwxrwxrwx. 1 root root 13 Jun 4 20:39 K35smb -> ../init.d/smb
lrwxrwxrwx. 1 root root 16 Jun 4 20:41 K36mysqld -> ../init.d/mysqld
lrwxrwxrwx. 1 root root 20 Jun 4 20:42 K36postgresql -> ../init.d/postgresql
lrwxrwxrwx. 1 root root 17 Jun 4 20:41 K50dnsmasq -> ../init.d/dnsmasq
lrwxrwxrwx. 1 root root 20 Jun 4 20:36 K50netconsole -> ../init.d/netconsole
lrwxrwxrwx. 1 root root 15 Jun 4 20:41 K50snmpd -> ../init.d/snmpd
lrwxrwxrwx. 1 root root 19 Jun 4 20:41 K50snmptrapd -> ../init.d/snmptrapd

---
/etc/inittab – Some Examples
/etc/inittab usually launches getty programs on one or more virtual terminals and does so for several different runlevels. Those are configured with lines like:
# Run gettys in standard runlevels
1:2345:respawn:/sbin/mingetty tty1
2:2345:respawn:/sbin/mingetty tty2
3:2345:respawn:/sbin/mingetty tty3
4:2345:respawn:/sbin/mingetty tty4
5:2345:respawn:/sbin/mingetty tty5
6:2345:respawn:/sbin/mingetty tty6
The first number reminds us of the virtual terminal where the getty runs; the next set of numbers are the several runlevels where this will happen (for example, launching mingetty in all of the runlevels 2, 3, 4, and 5).

---
/etc/inittab – Some Examples
Next is the action taken by the line. Some actions are "special". This action traps the Ctrl-Alt-Delete key sequence (regardless of runlevel) and shutdown system.
ca::ctrlaltdel:/sbin/shutdown -t3 -r now

---
/etc/inittab – Some Examples
On most RPM-based systems the graphical login screen is started in run level 5, where /etc/inittab runs a script called /etc/X11/prefdm. The prefdm script runs the preferred X display manager.
# Run xdm in runlevel 5
x:5:respawn:/etc/X11/prefdm -nodaemon

---
How to find current Runlevel
Command runlevel output previous and current runlevel
Command runlevel output previous and current runlevel
[root@localhost mostafa]# runlevel
3 5
[root@localhost mostafa]# runlevel
3 5
runlevel reads the system UTMP file, which defaults to /var/run/utmp when no alternate filename is given, to locate the most recent runlevel record.
During system boot, the environment variables RUNLEVEL and PREVLEVEL will be set by the init(8) daemon.
Command who with -r or --runlevel print current runlevel
[root@localhost rc5.d]# who -r
        run-level 5 2010-06-08 21:12

---
Finally /etc/rc.local
The rc.local file is for initialization of programs after the system has fully booted.
This script is run right before login prompts are displayed. We can use the file to run last minute startups, set certain environment variables, etc.
#!/bin/sh
#
# This script will be executed *after* all the other init scripts.
# You can put your own initialization stuff in here if you don't
# want to do the full Sys V style init stuff.
touch /var/lock/subsys/local

---
Changing Runlevel
One may switch init levels by issuing the init command with the appropriate runlevel. Use the command "init #" where # is one of s,S,0,1,3,5,6.
/sbin/telinit is linked to /sbin/init. It takes a one-character argument and signals init to perform the appropriate action.
0,1,2,3,4,5 or 6
tell init to switch to the specified run level.
a,b,c
tell init to process only those /etc/inittab file entries having runlevel a,b or c.
Q or q
tell init to re-examine the /etc/inittab file.
S or s
tell init to switch to single user mode.
U or u
tell init to re-execute itself (preserving the state). No re-examining of /etc/inittab file happens. Run level should be one of Ss12345, otherwise request would be silently ignored.

---
Creating your own run-level (HACK)
cd to /etc/rc.d/rc4.d/
do a sanity check to make sure you are running Red Hat: cat /etc/redhat-release
backup existing run-level directory:
mkdir /tmp/rc4.d.original/
cp /etc/rc.d/rc4.d/* /tmp/rc4.d.original/
rm -f /etc/rc.d/rc4.d/*
At this point
cp /etc/rc.d/rc1.d/* /etc/rc.d/rc4.d/

---
Creating your own run-level (HACK)
We have now copied the run-level scripts for single user mode into our own custom run-level 4. We can hijack the S99single script and tell it to do something different. In this example, we are going to write a custom Python script that gets forked to the background and backs up the machine over rsync. Let’s edit that file we copied:
vim /etc/rc.d/rc4.d/S99single
Change the last part of it to look like this:
# Now go to the single user level.
echo $"Telling INIT to go to single user mode."
echo "This is a custom code. Forking custom script"
/custom.py &
exec init -t1 S

---
Creating your own run-level (HACK)
We’ve inserted two lines. One echoes that we are forking off a custom script. The second line forks a python script, shown below, that backs up the machine via rsync. Note that this assumes you have set up ssh keys on the remote backup server. custom.py script:
#!/usr/bin/env python
import time
import subprocess
rsync = "rsync -av / 10.0.1.3:/Volumes/Backup/server_backup/"
network = "service network start"
init = "init 3"
cmds = [rsync, network]
def single_user_backup():
    """Starts network service, creates backup and returns to init 3"""
    try:
        subprocess.call(network, shell=True)
        subprocess.call(rsync, shell=True)
    finally:
        subprocess.call(init, shell=True)

---
Creating your own run-level (HACK)
def main():
    """Runs program"""
    print "sleeping for 60 seconds"
    #time.sleep(60) #Gives machine time to quiesce
    single_user_backup()
main()
The main function runs a sleep command for 60 seconds, just to give the single user mode scripts time to quiesce the box. Remember, this script is forked to the background. Next, function single_user_backup attempts to start network services and run rsync to remotely back up the whole / volume to another server. This is obviously crude and there will be lots of errors trying to back up /proc, for example, but it give you an idea of how an automated backup could work with a custom run-level. Finally, the machine gets called back to init 3, which is console only multi-user mode.

---
Init Script
A single copy of the script is located in the directory: /etc/rc.d/init.d/script-name (Red Hat/Fedora) or /etc/init.d/script-name (Ubuntu / Debian).
Use the command chkconfig to generate soft links to the appropriate directories for the various run levels.
[root@localhost init.d]# chkconfig
NetworkManager	0:off	1:off	2:on	3:on	4:on	5:on	6:off
abrtd	0:off	1:off	2:off	3:on	4:off	5:on	6:off
acpid	0:off	1:off	2:on	3:on	4:on	5:on	6:off
atd	0:off	1:off	2:off	3:on	4:on	5:on	6:off
auditd	0:off	1:off	2:on	3:on	4:on	5:on	6:off
avahi-daemon	0:off	1:off	2:off	3:on	4:on	5:on	6:off
backuppc	0:off	1:off	2:off	3:off	4:off	5:off	6:off
bluetooth	0:off	1:off	2:off	3:on	4:on	5:on	6:off
The bash script functions daemon, killproc and status can all be found in the script /etc/rc.d/init.d/functions. (Red Hat/Fedora distributions).

---
Init Script Sample Code
#!/bin/sh
#
# Startup script for program
#
# chkconfig: 345 85 15 - start or stop process definition within the boot process
# description: Description of program
# processname: process-name
# pidfile: /var/run/process-name.pid
# Source function library. This creates the operating environment for the process to be started
. /etc/rc.d/init.d/functions
case "$1" in
  start)
        echo -n "Starting process-name: "
        daemon process-name - Starts only one process of a given name.
        echo
        touch /var/lock/subsys/process-name
        ;;
  stop)
        echo -n "Shutting down process-name: "
        killproc process-name

---
Init Script Sample Code
        echo
        rm -f /var/lock/subsys/process-name
        rm -f /var/run/process-name.pid - Only if process generates this file
        ;;
  status)
        status process-name
        ;;
  restart)
        $0 stop
        $0 start
        ;;
  reload)
        echo -n "Reloading process-name: "
        killproc process-name -HUP
        echo
        ;;
  *)
        echo "Usage: $0 {start|stop|restart|reload|status}"
        exit 1
esac
exit 0

---
Init Script
The script must be executable to work. (chmod +x script-name).
The script may be used to start and stop processes. i.e.:
    * /etc/rc.d/init.d/httpd restart
      (Ubuntu / Debian / S.u.s.e.: /etc/init.d/apache2 restart)
    * /etc/rc.d/init.d/httpd stop
    * /etc/rc.d/init.d/httpd start
or use the Red Hat/Fedora core based service command:
    * service httpd restart
    * service httpd stop
    * service httpd start
Note that two lines in the script enable the chkconfig command to control the script for the boot and shutdown process.
    # chkconfig: 345 85 15
    # description: Description of program

---
chkconfig
The (Red Hat/Fedora/IRIX) chkconfig command generates and breaks links between the directory /etc/rc.d/init.d/ and the appropriate run level directory: /etc/rc.d/rc[0-6].d/ to control boot process initiation and process shutdown.
     chkconfig [--level ] on | off | reset >
     chkconfig --list
     chkconfig --list
     chkconfig --add
     chkconfig --del
     chkconfig --level 0123456 off

---
chkconfig
Examples:
    * chkconfig --level 345 httpd on - forces apache to be invoked for run levels 3, 4 and 5.
    * chkconfig --add httpd - Start the web server daemon upon system boot.
    * chkconfig --del sendmail - Do not start the sendmail daemon upon system boot.
    * chkconfig --list - List all services and init levels.
    * chkconfig --list | grep on - List all services to be started upon system boot.
Using chkconfig to administer xinetd processes.
    * chkconfig wu-ftpd on - Turn on FTP service managed by xinetd.
    * chkconfig ipop3 off - Turn off POP3 service managed by xinetd.
This will reconfigure the appropriate xinetd file (in directory /etc/xinetd.d/) and restart the xinetdprocess.

---
BSD-style
BSD init runs the initialization shell script located in '/etc/rc', then launches getty on text-based terminals or a windowing system such as X on graphical terminals. There are no runlevels; the 'rc' file determines how init is to be run.
Advantages: Simple and easy to edit manually.
Problems: If a 3rd-party package needs to have an initialization script run during the boot procedure, it needs to edit one of the existing boot scripts, but a simple mistake in that process could lead to an unbootable system.

---
SysV-style
System V init examines the '/etc/inittab' file for an 'initdefault' entry, which tells init whether there is a default runlevel. If there is no default runlevel, then the user is dumped to a system console, where a runlevel must be entered manually.
Advantages: Flexibility and scalability.
Problems: Complexity.

---
Other styles
Various efforts have been made to replace the traditional init daemons with something better.
SystemStarter, superseded by launchd — Apple Mac OS X's process spawner
Initng, a full replacement of init designed to start processes asynchronously
Upstart, a full replacement of init designed to start processes asynchronously initiated by Ubuntu
Service Management Facility, a complete full replacement/redesign of init from the ground up in Solaris starting with Solaris 10
runit, a cross-platform full replacement for init with parallel starting of services
BootScripts in GoboLinux
DEMONS, a modification of the init start process by KahelOS, where daemons are started only when the DE (desktop environment) started.
Mudur, an init replacement written in Python and designed to start process asynchronously in use by the Pardus Linux distribution.

---
Other styles
The following list are links to projects that are not (yet) in widespread use.
eINIT, a full replacement of init designed to start processes asynchronously, but with the potential of doing it without shell-scripts
svscan from daemontools used as process 1 - seems to be superseded by runit
cinit
twsinit, partly written in x86 assembler, more a proof of concept
Minit
OpenRC

---
Shutdown or Reboot System
Shutdown:
init 0
shutdown -h now
-a: Use file /etc/shutdown.allow
-c: Cancel scheduled shutdown.
halt -p
-p: Turn power off after shutdown.
poweroff
Reboot:
init 6
shutdown -r now
reboot
Enter single user mode:
init 1